## Slide 1: Using Spread Spectrum with Narrow Band Channels
June 21, 2026
George Elmasry, Raytheon’s System Engineering

## Slide 2: Spread Spectrum for Wireless Channels
Spread spectrum has the advantages of:
  Reducing detectability
  Mitigating various forms of fading
  Enhancing resilience to external and self-interference
Raytheon’s typical wireless radios use a combination of spread spectrum and frequency hopping to achieve resilience against eavesdropping and combat jamming
Spread spectrum is avoided for narrowband channels (10s of Hz) because the room (frequency band) for spreading is limited
Although needed, spread spectrum is avoided with narrow band channels

## Slide 3: Reviews
The use of spread spectrum with frequency hopping
Mixing frequency hopping and spread spectrum offers resilience against eavesdroppers and jammers.
It is hard to synchronize with the frequency sub-band at any given moment.
Even if there is sync, spread spectrum makes the signal appear as background noise.
With a narrowband channel, there is no room for frequency hopping and spread spectrum

## Slide 4: Reviews
The spread signal is like noise
The existence of harmonics is a telltale of a modulated symbol.
Increasing the spreading factor means decreasing the ratio of .
We should strive to at least line the main (center) harmonic of the spread signal within the sub-band frequency range, such that spreading makes the signal as close to low-power noise as possible.
Spread spectrum hides the RF signal
Frequency domain Spread v non-spread signal
Maximizing spreading with the narrowband channel is needed

## Slide 5: Review
Engineers strive to create orthogonal codes
This minimizes self-interference
  If we transmit 2 signals at the same time using the same frequency sub-band, the two signals would not interfere with each other because the spreading codes are orthogonal to each other
  Each is background noise to the other
The Hadamard matrix is a form of maximizing the number of orthogonal spreading codes for a given spreading factor
Orthogonal Spread Codes
What to do with a narrow band channel?
For a channel with a bandwidth in the range of 10s of Hertz, the spreading factor we can use is very small and can be meaningless
There is no room for frequency hopping
Alternatively, if we can increase the number of orthogonal spreading codes, we can hop (cycle) through spreading codes for evasion
If we can maximize the number of orthogonal spreading codes in the narrow band channel, we can compensate for the lack of combined frequency hopping and spread spectrum by cycling through spreading codes

## Slide 6: The Challenge
Maximize spread spectrum with narrowband channels
  It will allow us to leverage the advantages of spread spectrum
    Signal hiding
    Mitigate self and external interference
  It will allow us to hop between spreading codes for evasion
Some solutions generate a single polynomial or a limited number of known polynomials, given the channel’s parameters:
  For example, Kasami generator polynomial can produce a small set of Kasami sequences (primitive polynomial of degree n=6)
  The polynomials are Known -- the signal can be discovered
  No room for mitigating self and external interference
  Not enough entries for evasion
We need to maximize the spreading capability beyond the known limits

## Slide 7: The Solution
We are seeking a matrix-based, not a polynomial-based solution
Maximize spreading beyond known channel bandwidth limitations
A Hadamard matrix with a large set of orthogonal spreading codes for a long spreading factor
Although this matrix may not be considered suitable for the narrow-band channel, within this matrix, we can find subsets of orthogonal codes that can survive the channel’s limitations. Consider:
  The matrix can map to a rate per 2 seconds, a rate per 4 seconds, and so on. Some applications can transmit a signal every seconds where
  We have room for correcting lossy compression. The large matrix allows the receiver’s cross-correlation to mitigate some chip loss due to channel effects
We want to go beyond the channel rate in bits/sec and beyond known max spreading by considering lossy compression

## Slide 8: The Experimental Solution
We used MATLAB to generate a large Hadamard matrix
  We spread the signal beyond the channel's per-second bitrate limitations
We experimented with the entries of this matrix. We were able to:
  Identify a subset of spreading codes that can’t survive the channel even when the channel doesn’t introduce noise (noiseless channel).
    This subset is discarded since it can’t survive the channel’s lossy compression
  Assign to the rest of the entries in the matrix a rank based on each entry’s ability to survive the channel’s bandwidth limitation and a given signal-to-noise ratio (SNR)
  This means that if we know the channel’s SNR, the transmitter and receiver can switch (hop) between all the orthogonal spreading codes that can survive the channel’s SNR
The main aspects of the solution are:
(1) The consideration of lossy compression,
(2) The consideration of signal harmonics, and
(3) Invoking Set Theory (dynamic sets)

## Slide 9: The Sought Solution
Just as Hadamard matrices are known and can be found in MATLAB for given parameters, the solution should be implementable in MATLAB, where it defines:
  Hadamard matrices with large spreading factors
    Maximize spreading, to increase the pool of usable spread codes
  The channel’s bandwidth (Harmonics and lossy compression)
  A given SNR range
    SNR is dynamic, making the available pool of spreading codes dynamic
  Other parameters, such as fading
That solution will identify the suitable subset from the large Hadamard matrix and how the available pool of spreading code varies with SNR.

## Slide 10: Analogy
Shannon proved that there is no point in joint source and channel coding or modulation and channel coding, provided that optimum solutions are used at each stage
  Practical solutions proved otherwise
  The ideal optimization at each stage is achievable by joining the stages
  There are gains from joint source and channel coding and joint modulation and coding
Bandwidth limitation shouldn’t prevent us from maximizing spreading
What we seek is a joint solution. We join spreading with:
  The message’s time length. The message rate per seconds, where
  The channel bandwidth (impacts lossy compression and harmonics)
  The channel’s SNR
  Other channel parameters, such as fading
This is merely and analogy

## Slide 11: Hadamard Transformation
The solution may lie with the Hadamard transformation
Hadamard transformation is related to the Fourier Transformation
Lower harmonics in the Hadamard transformation are lower harmonics in the Fourier Transformation
Hadamard Transformation is already amended by:
  Walsh Ordering: Rows are reordered by increasing frequency
  Dyadic/Paley Ordering: Rows are ordered based on the binary Gray code
Aspect 1: Account for lossy compression in the channel:
Mapping the Walsh ordering to a channel bandwidth creates a set of usable codes for our channel
That set size can increase, considering how the receiver’s cross-correlation recovers additional entries
This leads to using a larger Hadamard matrix than was originally thought for the given channel
We can refer to Aspect 1 as joint lossy compression, Hadamard coding, and channel coding (inner error control coding)

## Slide 12: Hadamard Matrix
No Harmonics
Low Harmonics
Distance of 4

## Slide 13: What is in the literature, and what is missing
In the literature | Need complement
Mapping a set of low harmonics entries to a narrow band channel | Consider the impact of lossy compression and cross-correlation on additional entries
Finding sets with distance limits | Relating the distance/Gray code to lossy compression recovery and SNR
The ideal channel/no noise set
High SNR set
Lower SNR set
Lowest SNR set
Aspect 2: Invoke Set Theory
We can refer to Aspect 2 as joint Set Theory and maximizing the Hadamard matrix size

## Slide 14: Summary
There is a need to maximize spread spectrum with narrow band channels
The road to this maximization is to join:
  Lossy compression of the channel
  Hadamard transformation with respect to channel harmonics
  Replace channel coding (inner error control coding) with increased chip rate
  Invoke Set Theory
It is possible to assume digital binary phase shift keying modulation
  This will not impact the ability to create the desired joint solution
We desire the solution to be:
  Dynamic sets so that channel feedback can result in changes to the usable set
  implemented in MATLAB